## Slide 1: DTSE methodology
Brahim Al Farisi, Alexia Kourfali and Karel Heyse
Complex Systems Design Methodology – DTSE methodology – Ghent University – Academic year 2013-2014

## Slide 2: DTSE methodology
Data Transfer and Storage Exploration (DTSE)
Roadmap for a more efficient memory usage
Developed by our friends from

## Slide 3: Goal of the methodology
Improving memory usage
  Minimize memory
  Less memory accesses
  Improve data flow
In order to
  Reduce power consumption
  Reduce execution time

## Slide 4: Reduction of power consumption (1)
All accesses to the main memory
Power: 100% x 1 = 1
processor
data track
registers
main memory
100% accesses
1

## Slide 5: Reduction of power consumption (2)
Spread the accesses between the main memory and scratch pad memory
Power: 100% x 0.1 + 10% x 1 = 0.2
processor
data track
registers
main memory
scratch
10%
100%
1
0.1
Notes: Update image

## Slide 6: Meant for ….
Software and hardware
Data driven applications
  Processing of media (sound, images)
  Video compression

## Slide 7: Steps
Trimming and preparation
Dataflow transformations
Global loop transformations
Data reuse
Memory organization
Data structure optimization
Optimization of address calculation
Notes: Overview of steps to take

## Slide 8: 1. Trimming and preparation
Profiling
  Identifying hot code
Change the code
  Focus on useful code
  Reduction of complexity
  Increase exploration freedom (static single assignment form)

## Slide 9: 2. Dataflow transformations
Improve the dataflow in the program
Removal of useless memory accesses

## Slide 10: 3. Loop transformations
Improvement of temporal locality and regularity
Simple transformations

## Slide 11: 4. Data reuse
Exploiting the locality
Introduction of the memory hierarchy

## Slide 12: 5. Memory organization
Data grouping inside memories
Adding of timing constraints
Trade off between speed and power consumption

## Slide 13: 6. Data structure
Removal of static single assignment form
Storing two dimensional data in one dimension
Taking into account liveness of data
Place arrays into the same memory

## Slide 14: 7. Optimization of calculations
Simplifying address computation
Removing redundant control structures

## Slide 15: Results
accesses
size
clock cycles
100
200
300
400
500
Original
Data transformation
Loop transformation
Data reuse
Optimization

## Slide 16: Cavity detector
Standard example from IMEC
Medical image processing: computer tomography (CT)
Detection of holes on a CT scan

## Slide 17: Cavity detector
Algorithm in three steps
  Gaussian blurring (2 sub steps)
  Edge detection
  Detecting the actual cavities
Cooked up by an Medical Doctor
Different implementations can produce same result

## Slide 18: Gaussian blur (1)
Horizontal filtering
Filter coefficients: (2, 3, 2)
ct-scan.bmp becomes gtemp.bmp

## Slide 19: Gaussian blur (2)
Vertical filtering
Filter coefficients: (2, 3, 2)
gtemp.bmp becomes gaus.bmp

## Slide 20: Edge detection
Compare each pixel with all its neighbours
On an edge their difference will be big
The intensity of edge.bmp is maximal absolute difference

## Slide 21: Detect cavities
Convert edge.bmp into out.bmp (black-white)
Compare each pixel with its neighbours
  At least one lighter: color black
  Otherwise: color white

## Slide 22: 1. Trimming and preparation (1)
Focus on useful code
  Hide other code in separate files
  Example: input and output
Reduction of complexity
diff = gauss[x+k][y+l] - gauss[x][y];
diff = diff < 0 ? -diff : diff;
edge[x][y] = diff > edge[x][y] ?
diff : edge[x][y];
edge[x][y] = maxDiff(gauss[x][y],
gauss[x+k][y+l], edge[x][y]);

## Slide 23: 1. Trimming and preparation (2)
Increase the exploration freedom
  Dataflow is not always clear
int sum;
for (i=0; i<100; i++) {
sum = 0;
for (j=0; j<100; j++) {
sum += A[i][j];
}
... = f(sum);
}
i
j

## Slide 24: 1. Trimming and preparation (3)
Increase the exploration freedom
  Dataflow is not always clear
  Static single assignment form (SSA)
int sum[100];
for (i=0; i<100; i++) {
sum[i] = 0;
for (j=0; j<100; j++) {
sum[i] += A[i][j];
}
... = f(sum[i]);
}
explicit
dataflow
Notes: TODO: translation again

## Slide 25: 1. Trimming and preparation (4)
Overview code cavity detector
  testbench.cpp
  original.h, step1.h, step2.h
// testbench.cpp
#define NUMBER_OF_TEST_RUNS 10
#define COUNT_MEMORY_ACCESSES
#include "original.h"
// original.h
#define VERSION "original"
void cavityDetection(...);

## Slide 26: 1. Trimming and preparation (4)
original.h contains the original code
step1.h contains the code after trimming and preparation
Differences:
  New function maxDiff
  accux and accuy are in SSA form
Notes: TODO: afwerken

## Slide 27: 2. Dataflow transformations (1)
Remove useless memory accesses
  Data that is written but not read
  Propagation of data that is known in advance
Multiple ways to remove unnecessary data accesses
  Try to keep loops in the program
    Use additional conditions (if) within the loop body instead

## Slide 28: 2. Dataflow transformations (2)
Propagation of data that is known in advance
for (i=0; i<N; i++) A[i][0]=0;
for (j=1; j<M; j++) {
for (i=0; i<N; i++) {
A[i][j] = A[i][j-1] +
f(B[i], j);
}
}
i
j

## Slide 29: 2. Dataflow transformations (3)
Propagation of data that is known in advance
for (i=0; i<N; i++) A[i][1] = f(B[i], 1);
for (j=2; j<M; j++) {
for (i=0; i<N; i++) {
A[i][j] = A[i][j-1] + f(B[i], j);
}
}

## Slide 30: Assignment (1)
Download cavity detector (Minerva)
Compare original.h and step1.h
Make step2.h and extend
  Data that is never used
  Propagation of data that is know in advance
Automatically verifies result
  Check for differences via output-diff.bmp
Measure and compare with original.h
  Execution time and number of memory accesses

## Slide 31: Assignment (2)
Measure execution time and number of accesses separately
Edit the following to make appropriate measurements
// testbench.cpp
#define NUMBER_OF_TEST_RUNS 10
#define COUNT_MEMORY_ACCESSES
#include "original.h"